Maximal Stimulation Test  and Electroneurography (EnoG)

MST:  Stimulation at the areas shown            ENOG:  Maximal stimulation at the stylomastoid

above and the movements are observed..       foramen and the compound action potentials

measured on the cheek or in the nasolabial

fold.

The well known Hilger stimulator uses metal tips for stimulating over the face, and this can be

Painful.   When fitted with filt tips the stimulation is much less painful

ENOG as developed by Esslen. Filter tipped electrodes are used for

stimulation as well as for recording in the nasolabial fold.

The patient is very scared when the face paralises Therefore everything should be done to get information of the state of the nerve (threatening degeneration or not) and to determine the prognosis. This can be done in a very easy way by means of electrodiagnosis.  Electrodiagnosis of a facial palsy is easy, quick, and cheap if the Visual ENoG (VENOG) is used.  Referral to someone who has an ossiloscope and can do ENoG is not always necessary.

Needle electrode myography, as performed by neurologists and neurophysiologists do not give practical information in the beginning of an acute paralysis because the recording needle in the cheek only measures a single or a few fibres of the nerve. One needs to measure the performance of the nerve as a whole, i.e. obtain the compound action potentials (as advised by the late Esslen, neurologist, Aarau, Switzerland), which is easily done by means of stimulating at the stylomastoid foramen. The stimulation causes little pain if filt tipped electrodes are used. The result of the test is obtained immediately by observing the movement of the face when maximal stimulation is applied at the stylomastoid foramen (VENOG). To get an ENOG the compound action potentials are recorded from the cheek or nasolabial fold at the same time with an ossiloscope (also using filt tipped electrodes -  not painful at all).

Observation of the paralysis: is it partial or total?  It is unreliable to ask the patient to move the face and/or close the eyes. The normal moving side will cause movements on the affected side if the facial muscle are not pressed firmly against the skull in order ro prevent movements over the midline (which can be surprisingly strong, because the patient tries his best to move the face) – see drawing.